PVDF Film with Adhesive     32-5A and 37-10A

CS HYDE Company 800-461-4161

Lake Villa, IL  60046

PVDF-Stick Tape with pressure sensitive adhesive is an exclusive CS Hyde Tape. PVDF Tape is made with PVDF film with an Acrylic Pressure Sensitive Adhesive for ease of application, positioning and fastening.  PDVF Tape offers excellent chemical and corrosion resistance and has a high tensile strength.  Good thermal stability and can be used in applications up to 300°F.  Kynar® (PVDF) has extremely high purity which makes it a good candidate for food applications.  When specified, Kynar 740 FILM complies with FDA regulation 21 CFR 177.510, USDA, USP XX Class VI, 3A sanitary standards and meets ASTM D3222 resin specifications.  PVDF Tape also possesses high impact resistance and is tough and durable. Transparent with a  Peel-off liner.

PVDF (Kynar ®)  is strong and tough as reflected by its tensile properties and impact strength. Compared to many thermoplastics, PVDF (Kynar ®) has excellent resistance to creep and fatigue, yet in thin sections such as films, PVDF (Kynar ®) components are flexible and transparent. PVDF is stable to UV and the effects of weather.  In cold, heat, sunlight and humidity PVDF Film does not wear out or get brittle.  Low NBS smoke generation and superior LOI.

ADVANTAGES OF PVDF FILM Excellent chemical resistance Stable to UV & effects of weather Low NBS smoke generation & superior LOI Excellent transmittance of solar energy Excellent dielectric strength High Heat Resistance Excellent Physical & mechanical properties Resin FDA compliant Low permeability to water vapor & various other gases Excellent Light Transmittance Possible Sub for Tedlar®

KYNStick® Tape can be supplied with high tack adhesives.   Acrylic Adhesive offers good adhesion, chemical and environmental resistance.   Tape has a peel-away liner.

KYNStick® Tapes are available in with .005"  or .010" Kynar® film thickness.  Other thicknesses are available on a custom basis.  KYNStick® Tape is semi-transparent and relatively colorless.  Product Series is #32-_A (Acrylic)   Widths can be cut from narrow to wide. KYNStick® can also be die cut into custom shapes or sheeted by-the-foot.

# Technical Data - KYNStick® Kynar® Film Tape

| PROPERTY | DATA |
| --- | --- |
| Backing Material | Kynar® Film |
| Backing Thickness (in) | .005" or .010" |
| Adhesive System | Acrylic |
| Adhesive Thickness (in.) | .002” or .005" |
| Tensile Strength (pli) | 31.08 |
| Elongation (%) | 45.1 |
| Dielectric Breakthrough (kV) | 7.52 |
| Peel Strength (pli) | 3.53 |
| Max. Operating Temp. (F) | 300 |
| AVAILABILITY |
| Core Dia. (in) | 3" |
| Width (in.) | .125-36 |
| Roll Length | 36 – 60 yds |

Out gassing:    PVDF (Kynar ®) exhibits extremely low weight loss when exposed to high vacuum.

Light Transmittance:   Where opacity and transparency of films are important, light transmission can be a determining factor for the proper film choice.   Light transmittance=93%, Film Only.   Light Transmittance With Adhesive has not yet been determined but is expected to test very well.

Permeability to Gases:    PVDF (Kynar ®) film = Low permeability to water vapor & various other gases.

| Gases | cc-mils/100 in 2/24 frs - atm |
| --- | --- |
| CO2 | 5.5 |
| Nitrogen | 9.0 |
| Oxygen | 14.0 |
| Water Vapor | 2.6 (g-mil) |